## Slide 1
Isabella Dalisay Fernandez
University of Florida
Region II 2025 Student Conference, April 3-4th
Copyright © by Isabella Dalisay Fernandez
Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Review of Mishaps in Rendezvous and Proximity Operations

## Slide 2: Introduction
Rendezvous and Proximity Operations (RPO)
  Approach and interaction between spacecraft
Applications
  In-space Servicing, Assembly, and Manufacturing (ISAM)
    Refuel old satellites
  Orbital debris removal

## Slide 3: Why?
Why is this important?
  RPO missions are becoming more complicated and uncertain
  Can help avoid unnecessary costly mistakes
Why did I choose this project?

## Slide 4: Introduction
1990 STS-32
1992 STS-49
1997 Progress-Mir
2005 DART
2007 Orbital Express

## Slide 5: STS-32
[1]

## Slide 6: STS-32
Project Background
  Long Duration Exposure Facility (LDEF)
    Deployed 1984
  Columbia launched 1990
[2]

## Slide 7: STS-32
Project Execution
  Radar lock initiated before 2nd star tracker pass
  Radar acquisition occurred after Corrective Combination Maneuver (NCC) burn
  Radar data incorporated into navigation

## Slide 8: STS-32
Project Execution
  Radar range and radar range rate data began to degrade
  Navigation filter rejected the two measurements
  Mission control inhibited the data
  Star tracker pass was completed

## Slide 9: STS-32
Radar hardware introduced range measurement bias at extreme ranges
[2]

## Slide 10: STS-32
Lessons Learned
  Characteristics of sensors must be thoroughly documented

## Slide 11: STS-49
[3]

## Slide 12: STS-49
Project Background
  Attach Perigee Kick Motor (PKM) to INTELSAT VI (F-3)

## Slide 13: STS-49
Project Execution
  Capture bar unable to stay connected
  New capture technique using hands
  Targeting attempt could not converge
    Lambert targeting code was the source of targeting failure

## Slide 14: STS-49
Project Execution
  New GNC software reloading did not work
  Ti-Delay Maneuver
  Mission Control manually computed Ti
  Ti targeting attempts were successful
  PKM functioned successfully, INTELSAT continued its operations

## Slide 15: STS-49
Lambert Targeting Anomaly
  Anomaly did not occur in the first 35 times it was used throughout STS-49
  Assigning of single-precision values to double-precision variables
  Comparison of single-precision variables with double-precision variables

## Slide 16: STS-49
Lessons Learned
  Experienced and interdisciplinary flight control team
  Proper documentation and testing of changes made to code within iteration loops
  Proper review of analysis and technical reports
  Creation of documents describing software requirements for nonspecialists

## Slide 17: Progress-Mir
[4]

## Slide 18: Progress-Mir
Project Background
  Teleoperated Rendezvous Control System (TORU)
  Russian Control Center to position Progress above Mir
  TORU Operator Vasiliy Tsibliyev control Progress to dock with Mir
[5]

## Slide 19: Progress-Mir
Project Execution
  Tsibliyev’s screen was blank
  Screen worked after turning off emitter, ground control members manually calculated data
  Progress not visible in windows when it should have been in visual range

## Slide 20: Progress-Mir
[5]

## Slide 21: Progress-Mir
Project Execution
  A hole was punctured into Spektr, depressurizing the module
  Crew members sealed off the leak
  Reoriented Mir with help from ground control for solar panels to use sun

## Slide 22: Progress-Mir
Lessons Learned
  Sharing of information essential to mission success and safety
  The negative effects of economic and social pressure an organization is facing
  Safer redesigning of docking system > forced docking on faulty system
  Radio contact with ground control

## Slide 23: DART
[6]
[7]

## Slide 24: DART
Project Background
  Demonstration of Autonomous Rendezvous Technology (DART) spacecraft
    Not designed to receive commands from ground control
  Multiple Paths, Beyond-Line-of-Sight Communications (MUBLCOM) satellite

## Slide 25: DART
Project Execution
  Launch, early orbit, and rendezvous were completely successful
  DART started using more propellant than expected during proximity operations phrase
  DART detected it was out of propellant and initiated its department sequence
  Collided with MUBLCOM

## Slide 26: DART
Detail into mishaps
Differences between estimated and measured position
Computational resets
DART restarted estimated speed and position using GPS; but GPS was inaccurate
More differences between estimated and measured positions
Cyclic software resets
Extra thruster firings, excessive fuel usage
DART premature departure and retirement

## Slide 27: DART
Lessons Learned
  Quality of training and experience
  Rigorous GNC software development
  Management checks to prevent improper vehicle configurations from schedule pressure
  Risk assessments for high-priority flights

## Slide 28: Orbital Express
[8]

## Slide 29: Orbital Express
Project Background
  Demonstrate on-orbit satellite servicing autonomously
Autonomous Space Transfer and Robotic Orbiter (ASTRO)
Next generation Satellite/Commodity Spacecraft (NextSat/CSC)

## Slide 30: Orbital Express
Project Execution
  ASTRO’s sensor computer had major failure, making it miscalculate its position and orientation
  ASTRO drifted unexpectedly, approached NextSat at wrong angle
  Unplanned configuration, triggering an automatic safety abort
  Manual intervention from ground operators to stabilize system
  ASTRO was able to successfully dock with NextSat

## Slide 31: Orbital Express
Mishap details
  ASTRO’s sensor computer’s major failure causes ASTRO to execute abort procedure and the loss of autonomous rendezvous and capture sensor system (ARCSS) data
Navigation filter rejected data from IR sensor
Accumulation of errors in previous navigation data
Errors compound and further deteriorate the navigation fix

## Slide 32: Orbital Express
Lessons Learned
  Assumptions made regarding navigation
  Relevance of IR sensors
  Problems from interdependence between sensor and navigation software
  Interference from ground control

## Slide 33: Most Prominent Lessons Learned
Changes across systems must be thoroughly tested and properly documented.
  STS-32
  STS-49
  DART

## Slide 34: Most Prominent Lessons Learned
Be cognizant of the pressure a company may face and the effects of this pressure on projects.
  Progress-Mir
  DART

## Slide 35: Most Prominent Lessons Learned
Personnel and crew members should be interdisciplinary and well-experienced.
  STS-49
  DART

## Slide 36: Most Prominent Lessons Learned
Avoid designs that preclude intervention from ground control.
  STS-49
  Orbital Express
  DART

## Slide 37: Most Prominent Lessons Learned
Changes across systems must be thoroughly tested and properly documented.
Be cognizant of the pressure a company may face and the effects of this pressure on projects.
Personnel and crew members should be interdisciplinary and well-experienced.
Avoid designs that preclude intervention from ground control.

## Slide 38: References
[1] Uri, John. “35 Years Ago: STS-32 Returns the Long Duration Exposure Facility,” NASA, Jan. 2025,
https://www.nasa.gov/centers-and-facilities/johnson/35-years-ago-sts-32-returns-the-long-duration-exposure-facility/
[2] Goodman, J. “Lessons Learned From Seven Space Shuttle Missions,” NASA CR–2007–213697, Jan. 2007.
[3] Lethbridge, C. “STS-49 Fact Sheet,” Spaceline,
https://www.spaceline.org/united-states-manned-space-flight/space-shuttle-mission-program-fact-sheets/sts-49/
[4] Uri, John. “20 Years Ago: Space Station Mir Reenters Earth’s Atmosphere,” NASA, Mar. 2021,
https://www.nasa.gov/history/20-years-ago-space-station-mir-reenters-earths-atmosphere/
[5] Lilley, S., “Spektr of Failure,” NASA, Vol. 4, Nov. 2010.
[6] Kramer, H., “DART: Rendezvous,” eoPortal, May 2012.
[7] Wander, S. “Fender Bender,” NASA, Vol. 2, No. 7, Sept. 2008,
https://sma.nasa.gov/docs/default-source/safety-messages/safetymessage-2008-09-01dartsautomatedcollision.pdf?sfvrsn=f3a91ef8_4
[8] “Orbital Express Space Operations Architecture,” Tactical Technology Office, Feb. 2007, https://web.archive.org/web/20070313165744/http://www.darpa.mil/tto/programs/oe.htm