## Slide 2
Design Sub-Problems
Sub Problem: selecting airfoil based on their data, Reynolds number, and conceptual sketches
Measure of Success: Lift-to-Drag is the highest compared to other airfoils
DSP 1 - Airfoil Selection
DSP 2 - 3D CAD Model
Sub Problem: creating CAD models of BWB
Measure of Success: CFD analysis shows Lift is greater than upper limit of weight range at cruise conditions
2

## Slide 3
Methodology Flow Chart
Sub Problem: selecting airfoil based on their data, Reynolds number, and conceptual sketches
Measure of Success: Lift-to-Drag is the highest compared to other airfoils and is above 60
3) Chord Length Estimation
1) Conceptual Sketches
2) Cruise Speed Estimation
4) Reynolds Number Estimation
5) Airfoil Selection
6) CAD Modeling
7) CFD Simulation
8) Determine Lift & Drag
3
Notes: Mention iterative weight estimation

## Slide 4
Methodology Flow Chart - Airfoil Selection
1) Conceptual Sketches
2) Determine Kinematic Viscosity of Martian Atmosphere
3) Reynolds Number Estimation
4) Find Airfoil Models
5) Interpolate Data
6) Compare Data
7) Select Airfoil
8) Integrate Into CAD Model
4
Notes: Viscosity and atmospheric density of mars

## Slide 5
Mission Profile: MARVIN500
Cruise segment
Loiter segment
climb
descent
1
2
3
4
5
6
7
8
9
|—100 km—|
|—100 km—|
|———2 km———|
General survey & mapping
General survey & mapping
Survey land using various instruments
Survey land using various instruments
Range: 250 km
Loiter time: 30 mins each block
takeoff
landing
5

## Slide 6
Mission Profile: MARVIN5K
Sub Problem: selecting airfoil based on their data, Reynolds number, and conceptual sketches
Measure of Success: Lift-to-Drag is the highest compared to other airfoils and is above 60
Cruise segment
Loiter segment
climb
descent
landing
1
2
3
4
5
6
7
12
13
20 km
|——1 km——|
Test imaging & mapping
Range: 500 km
Loiter time: 30 mins each block
8
9
10
11
100 km
|—————2 km—————|
Imaging & Mapping
Imaging & Mapping
Imaging & Mapping
Land & Environmental survey
Land & Environmental survey
Land & Environmental survey
takeoff
100 km
100 km
6

## Slide 7
Mission Profile: MARVIN50K
takeoff
2
3
7
|—100 km—|
Cruise segment
Loiter segment
climb
1
4
5
6
8
9
|—100 km—|
|———2 km———|
Imaging & Mapping
Land & Environmental survey
descent
landing
13
|—100 km—|
|———120 km———|
|—100 km—|
Imaging & Mapping
Land & Environmental survey
14
15
12
11
10
Imaging & Mapping
Land & Environmental survey
Imaging & Mapping
Land & Environmental survey
Range: 600 km
Loiter time: 30 mins each block
7
Notes: This one uses net capture mechanism to retrieve aircraft

## Slide 8
Final Conceptual Sketches - MARVIN500
Top: defines shape and views
Bottom: modifies dimensions
8

## Slide 9
Final Conceptual Sketches - MARVIN5K
9

## Slide 10
Final Conceptual Sketches - MARVIN50K
10

## Slide 11
MOS: Maximized L/D
DSP1: Airfoil Selection

## Slide 12
Cruise Speed Estimation
Averaged cruise speed from past models
Not enough BWB models → general fixed-wing UAVs used
Model | Cruise Speed (m/s)
MARVIN500 | 62.23
MARVIN5K | 78.68
MARVIN50K | 197.37
12

## Slide 13
Airfoil Chord Estimation
Averaged wing width
Found from Conceptual Sketches
Model | Chord Length ft (m)
MARVIN500 | 6 (1.83)
MARVIN5K | 15 (4.57)
MARVIN50K | 25 (7.62)
Avg. Chord
Source
13

## Slide 14
Reynolds Number Estimation
Source
Re = vl/μ
  v → cruise speed
  l → characteristic length (chord length)
  μ → kinematic viscosity (0.000964 m2/s)
Model | Reynolds Number
MARVIN500 | 118,052.39
MARVIN5K | 373,154.12
MARVIN50K | 1,560,109.32
14

## Slide 15
Airfoil Models
Source
14
Airfoil Model
Sd7037
E387
E174
NACA6409
S7075
Notes: Add a chart before this showing all five airfoils

## Slide 16
Airfoil Data Interpolation
Source
14
Notes: Add a chart before this showing all five airfoils

## Slide 17
Airfoil Data Interpolation: MARVIN500
Source
14

## Slide 18
Airfoil Data Interpolation: MARVIN5K
Source
14

## Slide 19
Airfoil Data Interpolation: MARVIN50K
Source
14

## Slide 20
Airfoil Selection
Source
Data from airfoil database interpolated to find the L/D for aircraft based on its calculated Re
Data is tested and accurate; based on wind tunnel tests
MARVIN500: E174; L/D = 67.26
MARVIN5K: NACA6409; L/D = 110.60
MARVIN50K: NACA6409; L/D = 168.54
15

## Slide 21
MOS: Lift is greater than upper weight limit
DSP2: CAD Modeling

## Slide 22
CAD Models - MARVIN500
17
Notes: Show just isometric

## Slide 23
CAD Models - MARVIN5K
18

## Slide 24
CAD Models - MARVIN50K
19

## Slide 25
CFD Simulation Results
Parameters:
  Mars Environment, Gravity: 3.73 m/s2, Altitude: 2km, Initial velocity = cruise speed in x-direction
Average Lift and Average Drag values taken into consideration
Up to 300 iterations of CFD calculations per aircraft
Model | Average Lift (N) | L/D | Weight (N) | Payload Capacity (N)
MARVIN500 | 4,994.24 | 12.49 | 764.30 | 4,229.94
MARVIN5K | 28,907.7 | 7.38 | 7,643.03 | 21,263.97
MARVIN50K | 500,712 | 10.37 | 76,430.31 | 424,281.69
20

## Slide 26
Conclusions and Implications
Lift greater than upper limit of aircraft’s weight on Mars for all models
MARVIN models have the potential to fly on Mars
High-level MARVIN models can be integrated into future missions
Conclusions & Implications
Future Work
Velocity & pressure plots
Comparison to traditional aircraft
Dimensional Analysis
Configuration layout
Prototyping & wind tunnel testing
Pressure Plot for MARVIN500
Velocity Plot for MARVIN500
21

## Slide 27
Questions?
Thank you!

## Slide 29
References
Airfoil tools. (2019). Airfoiltools.com. Retrieved August 27, 2024 from https://airfoiltools.com
Airfoil tools: CLARK Y. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=clarky-il
Airfoil tools: E174. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=e174-il
Airfoil tools: E387. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=e387-il
Airfoil tools: NACA 0012-34. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=naca001234-il
Airfoil tools: NACA6409. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=n6409-il

## Slide 30
References
Airfoil tools: NASA SC(2)-0518. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=sc20518-il
Airfoil tools: S3014-095-85. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=s3014-il
Airfoil tools: S7075. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=s7075-il
Airfoil tools: SA7035. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=sa7035-il
Airfoil tools: Sd7037. (2019). Airfoiltools.com. Retrieved November 5, 2024 from http://airfoiltools.com/airfoil/details?airfoil=sd7037-il

## Slide 31
References
Airforce Technology. (2003, May 13). X-45 J-UCAV (Joint Unmanned Combat Air System). Airforce Technology. https://www.airforce-technology.com/projects/x-45-ucav/
Ansys. (n.d.). Quality assurance. Retrieved October 29, 2024 from https://www.ansys.com/company-information/quality-assurance
Bridgeman, L. (1947). Jane’s all the world’s aircraft 1974. Sampson Low, Marston, & Co.
Brown, D. (1970). Miles aircraft since 1925. Putnam.
Creech, G. (2013, April 17). X-48 research: All good things must come to an end. Nasa.gov. https://www.nasa.gov/centers-and-facilities/armstrong/x-48-research-all-good-things-must-come-to-an-end/

## Slide 32
References
Estes, A. (2013, February 6). The future of drone warfare is scary. The Atlantic Wire. https://web.archive.org/web/20131111073443/http://www.theatlanticwire.com/technology/2013/02/future-drone-warfare-is-frightening/61884/
First flight of the Elbit Systems Hermes 900 UAV - Defense update. (2009, December 9). Defense Update: - Military Technology & Defense News. https://defense-update.com/20091209_first-flight-hermes-900-uav.html
Fujita, K., Luong, R., Nagai, H., & Asai, K. (2012). Conceptual design of Mars airplane. Transactions of the Japan Society for Aeronautical and Space Sciences, Aerospace Technology Japan, 10(28), 5–10. https://doi.org/10.2322/tastj.10.te_5
Gelzer, C. (2010, February 11). X-48B blended wing body - NASA. Nasa.gov. https://www.nasa.gov/aeronautics/x-48b/

## Slide 33
References
Hidaka, H., & Okamoto, M. (2014). An experimental study of triangular airfoils for mars airplane. Transactions of the Japan Society for Aeronautical and Space Sciences, 12(ists29), p. 21-27. https://doi.org/10.2322/tastj.12.pk_21
Jackson, P. (2000). Jane’s all the world’s aircraft, 2000-2001. Jane’s Information Group.
Kim, H. D. (2010, September 19). Distributed propulsion vehicles. International Congress of the Aeronautical Sciences. 27th International Congress of the Aeronautical Sciences, Nice, France. https://ntrs.nasa.gov/citations/20100036222
Leifsson, L. T., Ko, A., Mason, W. H., Schetz, J. A., Haftka, R. T., & Grossman, B. (2005). Multidisciplinary design optimization for a blended wing body transport aircraft with distributed propulsion. Aerospace Science and Technology, 25(1). https://doi.org/10.1016/j.ast.2011.12.004

## Slide 34
References
Lyu, Z., & Martins, J. R. R. A. (2014). Aerodynamic design optimization studies of a blended-wing-body aircraft. Journal of Aircraft, 51(5), 1604–1617. https://doi.org/10.2514/1.c032491
McDonnell XP-67. (1999). Www.joebaugher.com. https://www.joebaugher.com/usaf_fighters/p67.html
NASA Glenn Research Center. (2023). N3-X. Grc.nasa.gov. https://www1.grc.nasa.gov/aeronautics/eap/airplane-concepts/n3x/
Navy unmanned combat air system advanced development program office Navy UCAS ADPO. (2012, August 17). Archive.org. https://web.archive.org/web/20170420235706/https://www.slideserve.com/conroy/navy-unmanned-combat-air-system-advanced-development-program-office-navy-ucas-adpo

## Slide 35
References
Northrop Grumman. (2020). Bat UAS: family of multi-mission, persistent and affordable tactical unmanned aircraft systems. https://cdn.northropgrumman.com/-/media/wp-content/uploads/BAT_Datasheet.pdf?v=1.0.0
Onshape. (n.d.). Why Onshape?. Retrieved October 29, 2024 from https://www.onshape.com/en/why-onshape
Rajarajan, S., Surya, P., Karthikeyan, M., Manikandan, P., & Lokeshkumar, K. (2021). Numerical study of unconventional airfoils at low Reynolds number for the application of Mars flight. International Journal of Applied Engineering Research, 16(5), 362-371. https://doi.org/10.13140/RG.2.2.33666.20163
Raymer, D. P. (1992). Aircraft design: A conceptual approach. American Institute of Aeronautics and Astronautics.
RUSI. (2024). Hermes 900 UAV. RUSI | Armed Drones in the Middle East. https://drones.rusi.org/drone-inventory/

## Slide 36
References
Simscale. (2023, March 16). What is CFD | Computational fluid dynamics? Simscale. Retrieved October 29, 2024 from https://www.simscale.com/docs/simwiki/cfd-computational-fluid-dynamics/what-is-cfd-computational-fluid-dynamics/
SOLIDWORKS. (2017, November 28). SOLIDWORKS Flow Simulation. Retrieved October 29, 2024 from https://www.solidworks.com/product/solidworks-flow-simulation
Şugar-Gabor, O., & Koreanschi, A. (2020). Design of supercritical low-Reynolds-number airfoils for fixed-wing flight on Mars. Journal of Aerospace Engineering, 33(5). https://doi.org/10.1061/(asce)as.1943-5525.0001166
The National Academies of Science Engineering Medicine. (2020). Leveraging unmanned systems for Coast Guard missions. https://doi.org/10.17226/25987

## Slide 37
References
U.S. Air Force. (2015a, September 23). MQ-1B Predator. U.S. Air Force. https://www.af.mil/About-Us/Fact-Sheets/Display/Article/104469/mq-1b-predator/
U.S. Air Force. (2015b, September 23). MQ-9 Reaper. U.S. Air Force. https://www.af.mil/About-Us/Fact-Sheets/Display/Article/104470/mq-9-reaper/
Walker, D. D. (2008). Preliminary design, flight simulation, and task evaluation of a Mars airplane. TRACE: Tennessee Research and Creative Exchange. https://trace.tennessee.edu/utk_gradthes/496/