## Slide 1
Matthew Rickman
Jake Peterson
Alder Louviere
Mississippi State University
2025 Region II Student Conference, 3 April 2025 – 4 April 2025
Copyright © by Matthew R., Jake P., Alder L. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Variable Length, Drag-Reducing Aerospike

## Slide 2: Team
From Left to Right: Matthew Rickman, Alder Louviere, Jake Peterson

## Slide 3: Background
Space Cowboys
Mach 2+ Flight Profile
30,000 Feet

## Slide 4: What is an Aerospike?
Thin structure that creates a detached shock
Used in lieu of a nose cone
Reduces drag at supersonic speeds

## Slide 5: Problem Statement
Drag-reducing, variable-length aerospike
Optimized performance throughout flight profile
Transonic to low-supersonic

## Slide 6: Objectives
Create baseline geometry for ANSYS Fluent testing
Evaluate spike configurations
Determine optimal spike geometry for each Mach

## Slide 7: Initial ANSYS Progress
Started out with basic 2D airfoils to learn the software
Mach 0.8 flow
Coarse Grid (~50,000 elements)

## Slide 8: NCPA Test and Calibration
Had aerospike geometry tested at NCPA
Used the data to validate 3D CFD setup
NCPA Schlieren
ANSYS Simulation

## Slide 9: Full-Scale 3D CFD
Scaled models up to 6-inch diameter
Mesh grew from ~100,000 elements to ~5 million
Computation time ballooned to 10 hours per run

## Slide 10: Limitations
Computational power
  Shift to axisymmetric design
  Simplified geometry
Small selection of prior research for this geometry and flight profile

## Slide 11: Updated Methodology
2D, Axisymmetric model
  Constant diameter aerospike, only varying length
  One reference model without an aerospike
  Divide computation between multiple computers
  Goal: Determine the optimal spike length for each Mach

## Slide 12: Optimizing Steps
Start with a length estimate:
    6-in for Mach 0.8 and 1, 9-in for Mach 1.25 and 1.5, and 12-in for Mach 2.0
Calculate Cd for the starting length and ± 1-in:
    Pursue the direction with the lowest Cd
If both directions are worse:
    Change to ± 0.2-in and continue until the lowest value is found

## Slide 13: ANSYS – Reference Geometry
100-in. main body, 6-in. diameter, sub-divided
Axisymmetric

## Slide 14: ANSYS - Geometry
100-in. main body, 6-in. diameter, sub-divided
1-in. diameter aerospike, various length
Axisymmetric

## Slide 15: ANSYS – Mesh
0.2-in element size
~250,000 total elements, varied based on the aerospike length

## Slide 16: ANSYS – Simulation
K-omega SST turbulence model
All simulations were performed at sea-level conditions for simplicity
Utilized pressure far fields to modify the freestream Mach number for each run

## Slide 17: Mach 0.8 Contours
Reference
Aerospike
Almost identical contours due to freestream Mach being subsonic, so no large shockwaves are formed

## Slide 18: Mach 1 Contours
High drag shock
Lower drag shock
Reference
Aerospike

## Slide 19: Mach 1.25 Contours
Strong bow shock
Slightly weaker bow shock
Reference
Aerospike

## Slide 20: Mach 1.5 Contours
Strong bow Shock
Weak bow shock
Reference
Aerospike

## Slide 21: Mach 2 Contours
Strong bow Shock
Weak bow Shock
Reference
Aerospike

## Slide 22: Cd Comparisons
Almost a 50% reduction across all Mach numbers
Mach | Refence Cd | Optimum Length | Cd | % Reduction | Average Cd % Reduction
0.800 | 2.270 | 9.200 | 1.175 | 48.245 | 48.758
1.000 | 2.551 | 10.000 | 1.555 | 39.030 | 
1.250 | 2.933 | 10.400 | 1.459 | 50.241 | 
1.500 | 3.149 | 9.400 | 1.510 | 52.044 | 
2.000 | 3.358 | 9.600 | 1.537 | 54.230 | 
Chart: Mach Number
| 0.8 | 1 | 1.25 | 1.5 | 2
Cd | 1.1751 | 1.5551 | 1.4592 | 1.5102 | 1.537
Refence Cd | 2.2705 | 2.5506 | 2.9325 | 3.1491 | 3.3582
Chart: Mach Number
| 0.8 | 1 | 1.25 | 1.5 | 2
Optimum Length | 9.2 | 10 | 10.4 | 9.4 | 9.6

## Slide 23: Conclusions/Practical Uses
Aerospike usage not recommended for a Space Cowboys rocket
  Higher velocity flight
  Flight with a longer time at supersonic speeds
  Aerodynamic stability is unknown

## Slide 24: Future Work
Mesh-independent study
Test more parameters
Similar testing for a more appropriate flight profile
Construct and test a physical model

## Slide 25: Acknowledgements
Dr. Keith Koenig
Dr. Shreyas Narsipur