## Slide 1
Integrated State Estimation Development for Actively Controlled Rockets
Hridai Ambati, Patrick Barry, Kandarp Vadia, Albert Zheng
AIAA 2025 Region II Student Conference
4/3/2025 – 4/4/2025
Copyright © by Guidance, Navigation, and Control Project Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.

## Slide 2
WHO WE ARE
GEORGIA TECH GUIDANCE, NAVIGATION, AND CONTROL
We are the first collegiate team to demonstrate jet vanes thrust vectoring in a physical test.
To become the first collegiate team to utilize jet vanes in a rocket launch.
Mission for 2024-25

## Slide 3
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks

## Slide 4
Motivation and Overview for State Estimation
6-DOF Simulations
Sensor Models
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational
Estimation
Flight Software Implementation
Ground Phase
Infrastructure
In-Flight Phase
In-House Simulations

## Slide 5
Overview of Extended Kalman Filter
Why Kalman Filter? | Sensors are noisy Some variables can’t be directly measured
Step 1: Predict | Predict state in next time step given current state Predict future uncertainty
Step 2: Update | Measurements + predictions filtered estimate
Idea | Predict + update loop convergent estimate
Why Extended? | Dynamics and measurements are nonlinear Linearization is powerful
Why Kalman Filter? | Sensors are noisy Some variables can’t be directly measured
Step 1: Predict | Predict state in next time step given current state Predict future uncertainty
Step 2: Update | 
Idea | 
Why Extended? | Dynamics and measurements are nonlinear Linearization is powerful
Term | Meaning
x | State vector; the quantities being estimated
z | Measurement vector; the quantities being sensed
 | State transition function; predicts the state at the next time step using system dynamics
 | Measurement function: converts the state into the form of the measurement
Q | Process noise covariance matrix; represents uncertainty in the dynamics
R | Measurement noise covariance matrix; represents uncertainty in the measurements
P | State covariance matrix; represents level of belief in state estimate
Term | Meaning
x | State vector; the quantities being estimated
z | Measurement vector; the quantities being sensed
 | State transition function; predicts the state at the next time step using system dynamics
 | Measurement function: converts the state into the form of the measurement
Q | Process noise covariance matrix; represents uncertainty in the dynamics
R | Measurement noise covariance matrix; represents uncertainty in the measurements
P | State covariance matrix; represents level of belief in state estimate

## Slide 6
Extended Kalman Filter
Predict
Initialize
State Estimate Output
Refine state
Update
Measurement
,
(State to Sensor Mapping)
Predict next state
Predict next uncertainty
(Dynamic Model)

## Slide 7
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks

## Slide 8
Sensor Modeling
  Navigation requires reference trajectory
    Team developed 6-DOF closed-loop dynamical simulation (position, velocity, attitude)
    Used custom Flat Earth frame, ignoring Earth’s curvature and rotation
  Key usage of reference trajectory in sensor model generation
    Models add fake noise and error, emulating real sensor data (replace measurement vectors in algorithm)
    Custom accelerometer, gyroscope, magnetometer, GPS
Notes: 1) First step to State Estimation is sensor modelling
2) Testing important considering limited launch cadence of collegiate rocketry
3) Testing requires ref trajectory as truth data and a set of sensor models
4) As a result, the team developed a closed-loop dynamical sim generating a trajectory (including p, v, attitude of the rocket)
5) Sim is plugged into diff eq solver, and uses standard 6-DOF EOM and integrated controls (CFD-derived Aerodynamics, and thrust allocation curves from static fire data)
6) Key usage of ref traj in generating sensor models, which serve to emulate real sensor data by adding fake noise and error and aim to replace z vectors in nav algs
7) Team developed custom acc, gyro, magnetometer, GPS
- High-level eqs (B = turn on bias, eta = gaussian noise, Rbf = rotation matrices from body to Flat Earth frame)
- Custom Flat Earth frame, which ignores Earth's curvature & rotation (origin at launchpad, x-axis upward, y-axis downrange, and z-axis completing RHR)

## Slide 9
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks

## Slide 10
Bias Estimation
Static dynamics
Predict
Initialize
State Estimate Output
Estimate biases
Update
Measurement
,
(Accelerometer/Gyroscope Biases)
(Sensor to Bias Mapping)
1
2
4
3
5

## Slide 11
Bias Estimation

## Slide 12
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks

## Slide 13
Update
Initial Attitude Estimation
Static dynamics
Predict
Initialize
State Estimate Output
Estimate quaternion
Measurement
,
(Refined Initial Quaternion)
Normalize
(Sensor to Quaternion Mapping)
1
2
3
4
5
6
Initialize

## Slide 14
Update
Initial Attitude Estimation
Static dynamics
Predict
Initialize
State Estimate Output
Estimate quaternion
Measurement
,
(Refined Initial Quaternion)
Normalize
(Sensor to Quaternion Mapping)

## Slide 15
Update
Initial Attitude Estimation
Static dynamics
Predict
Initialize
State Estimate Output
Estimate quaternion
Measurement
,
(Refined Initial Quaternion)
Normalize
(Sensor to Quaternion Mapping)

## Slide 16
Update
Initial Attitude Estimation
Static dynamics
Predict
Initialize
State Estimate Output
Estimate quaternion
Measurement
,
Normalize
(Refined Initial Quaternion)
(Sensor to Quaternion Mapping)
1
2
3
4
5
6
Initialize

## Slide 17
Update
Initial Attitude Estimation
Static dynamics
Predict
Initialize
State Estimate Output
Estimate quaternion
Measurement
,
Normalize
(Refined Initial Quaternion)
(Sensor to Quaternion Mapping)
1
2
3
4
5
6

## Slide 18
Initialize

## Slide 20
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks

## Slide 21
  Need to have knowledge of rocket’s attitude in flight
    Caveats:
      Sensors used in ground estimation carry more uncertainty in flight
      Attitude dynamics untrustworthy
  Solution: propagate gyroscope measurements directly
    Major downside is integration drift, but...
      Short flight
      High-quality sensor
In-Flight Attitude Estimation

## Slide 22
In-Flight Attitude Estimation: The Algorithm
Initial “launchpad attitude” from ground estimation
Take gyroscope measurements:
Form instantaneous rotation quaternion,
Update quaternion estimate,

## Slide 23
In-Flight Attitude Estimation: The Algorithm
Initial “launchpad attitude” from ground estimation
Take gyroscope measurements:
Form instantaneous rotation quaternion,
Update quaternion estimate,

## Slide 24
In-Flight Attitude Estimation: Results

## Slide 25
In-Flight Attitude Estimation: Results

## Slide 26
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks

## Slide 27
Accelerometer Lever Arm
  Acceleration of CG Acceleration of IMU
Assumptions
CG position changes at a fixed rate
IMU is fixed on the body
Negligible angular accelerations

## Slide 28
Global Positioning System
Longitude (𝜆)
Latitude (𝜙)
Altitude (h)
WGS84 ellipsoidal equations
y (ECEF)
x (ECEF)
y (ECEF)
Local Rotation
North-East-Down Frame
Flat Earth Frame
GPS Coordinate Transformation
Earth-Center, Earth-Fixed
x
y
z
LLA

## Slide 29
In-Flight Estimation
Predict
Initialize
State Estimate Output
Estimate state
Measurement
,
(Refined State Estimate)
Update
Translational kinematics
IMU
GPS
Attitude Estimator
1
2
4
3
5
6
Predict
Notes: Remarks - now you can see how the past 3 algorithms are just key infrastructure to support the success of this algorithm

## Slide 30
In-Flight Estimation
Predict
Initialize
State Estimate Output
Estimate state
Measurement
,
(Refined State Estimate)
Update
Translational kinematics
IMU
GPS
Attitude Estimator
1
2
4
3
5
6
Notes: Remarks - now you can see how the past 3 algorithms are just key infrastructure to support the success of this algorithm

## Slide 31
Predict

## Slide 32
Notes: This is what we just described but in algorithm form. Note the update step and uncertainty propagation are explicitly mathematically expressed here rather than being treated as a black box, which we have done all presentation.

## Slide 33
In Flight Translational Navigation

## Slide 38
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks

## Slide 39
Flight Software Implementation
  Jet Vanes Rocket avionics: two custom PCBs
  STM32 microcontrollers run code written in C
    State estimation tasks on one MCU only
  In-flight algorithms running at 30 Hz
  State machine updates rocket’s phase of flight

## Slide 40
Flight Software Implementation
Jet Vanes Rocket Avionics
Power Management
Vaney
PCB 2
PCB 1
STM32 Microcontrollers
Software written in C
1st MCU
State Estimation
2nd MCU
In-Flight Algorithms
State Machine
Updates Rocket’s Phase of Flight

## Slide 41
Sensor Modeling
Bias Estimation
Initial Attitude Estimation
In-Flight Attitude Estimation
In-Flight Translational Estimation
Overview
Flight Software Implementation
Concluding Remarks
  End-to-end development process of state estimation from scratch
  Four key state estimation algorithms
  Future work: Improve on the nuts and bolts
Concluding Remarks

## Slide 43
THANK YOU