## Slide 1
Nishant Sood
IDREEM Lab, George W. Woodruff School of Mechanical Engineering
AIAA Region II Student Conference, 3rd–4th April 2025
Copyright © by Nishant Sood Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
1111
Design and Fabrication of an EDS-Enabled Brush Prototype for
Lunar Dust Mitigation

## Slide 2: Introduction
Evidence of a Lunar dust layer
  Apollo Missions
  Lunar Ejecta and Meteorites Experiment (LEAM)
Challenges posed by lunar dust include:
  Health, mechanical wear, thermal control, etc.

## Slide 3: Introduction
Proposed Solutions
  Simple Brushes
  Electrodynamic Dust Shield (EDS) Systems
Source: Calle et al., Integration of the Electrodynamic Dust Shield on a Lunar Habitat Demonstration Unit, Fig 2

## Slide 4: Past Work
Georgia Tech Team - “Shoot for the Moon”
Integrating EDS capabilities into a mechanical brush
  Initial prototype:

## Slide 5: Past Work
Shorting in metal components
Inflexible electrodes
Demonstrated EDS feasibility
Limitations arose from the manufacturing/design of the brush

## Slide 6: Defining Design Parameters
Prototype Component | Previous Implementation | Considerations
Electrodes | 3D Soldered wire grid | • ±0.5mm Tolerance on electrode spacing • Ease of electrode array assembly • Physical shorting/arcing prevention, flexible electrodes
Bristles | Whole brushes between electrodes | • Ensure any conductive metal components are insulated • Electrodes enmeshed in bristles
Structure | 3D Printed and fastened | Ease of assembly and sufficient insulation to electrodes • Support for bristles/electrodes • Sufficient tolerances for the electrode array

## Slide 7: Proposed Solution
Addressing improvements on the previous system
  Operational brushing
  Manufacturing tolerances
  Electrode efficacy
  Economical for rapid prototyping and design validation

## Slide 8: Prototype Design
PCB for electrode array
  Allows for tight tolerances between electrodes
  More economical/rapid prototyping
Epoxy Resin Structure
  Retains bristles through resin-set techniques
  Acts as a dielectric to insulate electrode bases.

## Slide 9: Prototype Design - Manufacturing

## Slide 10: Prototype Design – PCB Details
Wiring configuration for a 3 phase EDS operation
2D layout of 3 phase EDS operation

## Slide 11: Prototype Design
Multilayer 3 phase EDS operation

## Slide 12: Final Prototype Design
Electrode material
  Insulation
  Flexibility
  Brushing
Bristle material
  Nylon

## Slide 13: Conclusion and Future Work
Manufacturing test articles
Evaluating performance using lunar simulant in vacuum chambers
Validate design and inform future iterations

## Slide 14
This work was directly supported by the NASA Solar System Exploration Research Virtual Institute (SSERVI) under Cooperative Agreement #NNH22ZDA020C, Center for Lunar Environment and Volatile Exploration Research (CLEVER).
Acknowledgements